## Slide 1: Module 4
Planning and Implementing a Backup Strategy
Notes: The 20462C-MIA-SQL virtual machine used in the lab for this module includes a lot of software services that can take a while to start. For the best experience, have students start the 20462C-MIA-DC and 20462C-MIA-SQL virtual machines at the beginning of the module so that the services have time to start before students begin the lab.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 2: Module Overview
Understanding SQL Server Recovery Models Planning a Backup Strategy Backing up Databases and Transaction Logs Using Backup Options Ensuring Backup Reliability
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 3: Lesson 1: Understanding SQL Server Recovery Models
Overview of SQL Server Transaction Logs Transaction Log File Structure Working with Recovery Models Capacity Planning for Transaction Logs Working with Checkpoint Options Demonstration: Logs and Full Recovery
Notes: Students might be surprised that a module on backup begins with a discussion of the transaction log. Emphasize the importance of understanding how the transaction log and database recovery model affects backup and restore operations.
Question
You are about to import a large quantity of data into a SQL Server database by executing a generated T-SQL script. You want to ensure optimum performance. Which recovery model should you use while the import is running?
( )Option 1: The simple recovery model
( )Option 2: The full recovery model
( )Option 3: The bulk-logged recovery model
( )Option 4: Continue to use whichever model you were already using.
Answer
(√) Option 3: The bulk-logged recovery model
20462D
4: Planning and Implementing a Backup Strategy

## Slide 4: Overview of SQL Server Transaction Logs
Transaction logs provide a history of actions executed by a database management system to guarantee atomicity and durability of transactions
Buffer cache
2. Data pages are located in, or read into, the buffer cache and then modified
3. Modification is recorded in transaction log on disk
4. Later, checkpoint writes
dirty pages to data files
1. Data modification is
sent by application
Notes: Point out that the purpose of the transaction log is to confirm the atomicity, consistency, isolation, and durability (ACID) properties of transactions.
Describe the WAL protocol in detail.
Don’t go into too much detail on recovery yet, as it will be discussed in the restore module.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 5: Transaction Log File Structure
Sufficient information is logged to be able to:
  Roll back transactions if requested
  Recover the database in case of failure
Write Ahead Logging is used to create log entries
  Transaction logs are written in chronological order in a circular way
  Truncation policy for logs is based on the recovery model
Notes: Point out that the MinLSN is the start of the oldest active transaction in the database. All records with a value greater than that can never be truncated as they are needed for a potential recovery.
Stress, though, that replication can also prevent log truncation.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 6: Working with Recovery Models
Recovery Model | Description
Simple | Does not permit or require log backups Automatically truncates log to keep space requirements small
Full | Requires log backups for manageability Avoids data loss due to a damaged or missing data file Permits recovery to a specified point in time
Bulk Logged | Requires log backups for manageability Can enhance the performance of bulk copy operations Reduces log space usage by using minimal logging for many bulk operations
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 7: Capacity Planning for Transaction Logs
Capacity needs are based on several factors:
  Recovery model used for the database
  Transaction log backup frequency in full and bulk logged recovery models
  Number and size of transactions in the database
Examine log behavior during pre-deployment testing
Notes: Emphasize why the recovery model has a big impact on the log capacity needed within a database.
Point out that truncation is really only happening after a log backup and a full database backup has no influence on it. There are common misconceptions around this.
Discuss how to measure the number and size of transactions occurring on the system. Point out that, often, the best way is to measure log file needs during the pre-deployment tests on the system.
Mention that other features might also prevent log truncation and need to be considered, including database mirroring, transactional replication, change data capture (CDC).
Briefly describe the process for truncating excessively large log files.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 8: Working with Checkpoint Options
Types of checkpoint operations:
  Automatic
  Indirect
  Manual
  Internal
CHECKPOINT statement configures the target recovery duration
Notes: Explain the four types of checkpoint operations, ensuring that students understand why each type occurs.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 9: Demonstration: Logs and Full Recovery
In this demonstration, you will see how to:
Observe log file behavior in the Full recovery model
Notes: Tell students not to worry about the BACKUP syntax at this point – it will be discussed in more detail later.
Preparation Steps
Start the 20462C-MIA-DC and 20462C-MIA-SQL virtual machines.
Demonstration Steps
Observe Log File Behavior in the Full Recovery Model
Ensure that the 20462C-MIA-DC and 20462C-MIA-SQL virtual machines are running, and log on to 20462C-MIA-SQL as ADVENTUREWORKS\Student with the password Pa$$w0rd.
In the D:\Demofiles\Mod04 folder, run Setup.cmd as Administrator.
Start SQL Server Management Studio and connect to the MIA-SQL database engine using Windows authentication.
In Object Explorer, expand Databases, right-click the LogTest database, and click Properties.
In the Database Properties - LogTest dialog box, on the Options page, verify that the Recovery model is set to Full. Then click Cancel.
Open the LogsAndFullRecovery.sql Transact-SQL file in the D:\Demofiles\Mod04 folder.
Select the code comment Perform a full database backup and click Execute.
Select the code comment View database file space and click Execute. Note the space used in the LogTest_log file (and note that log files have a type value of 1).
Select the code comment Insert data and click Execute to insert 5000 rows.
Select the code comment View log file space and click Execute. Note the space used in the LogTest_log file has increased.
Select the code comment Issue a checkpoint and click Execute force SQL Server to perform a checkpoint and flush the modified pages to disk
Select the code comment View log file space again and click Execute. Note the space used in the LogTest_log file has not decreased.
Select the code comment Check log status and click Execute. Note that SQL Server is awaiting a log backup before the log file can be truncated.
20462D
4: Planning and Implementing a Backup Strategy
(More notes on the next slide)

## Slide 10
Notes: Select the code comment Perform a log backup and click Execute.
Select the code comment Verify log file truncation and click Execute. Note the space used in the LogTest_log file has decreased because the log has been truncated.
Keep SQL Server Management Studio open for the next demonstration.
Observe Log File Behavior in the Full Recovery Model
Ensure that the 20462C-MIA-DC and 20462C-MIA-SQL virtual machines are running, and log on to 20462C-MIA-SQL as ADVENTUREWORKS\Student with the password Pa$$w0rd.
In the D:\Demofiles\Mod04 folder, run Setup.cmd as Administrator.
Start SQL Server Management Studio and connect to the MIA-SQL database engine using Windows authentication.
In Object Explorer, expand Databases, right-click the LogTest database, and click Properties.
In the Database Properties - LogTest dialog box, on the Options page, verify that the Recovery model is set to Full. Then click Cancel.
Open the LogsAndFullRecovery.sql Transact-SQL file in the D:\Demofiles\Mod04 folder.
Select the code the comment Perform a full database backup and click Execute.
Select the code comment View database file space and click Execute. Note the space used in the LogTest_log file (and note that log files have a type value of 1).
Select the code comment Insert data and click Execute to insert 5000 rows.
Select the code comment View log file space and click Execute. Note the space used in the LogTest_log file has increased.
Select the code comment Issue a checkpoint and click Execute force SQL Server to perform a checkpoint and flush the modified pages to disk
Select the code comment View log file space again and click Execute. Note the space used in the LogTest_log file has not decreased.
(More notes on the next slide)
20462D
4: Planning and Implementing a Backup Strategy

## Slide 11
Notes: Select the code comment Check log status and click Execute. Note that SQL Server is awaiting a log backup before the log file can be truncated.
Select the code comment Perform a log backup and click Execute.
Select the code comment Verify log file truncation and click Execute. Note the space used in the LogTest_log file has decreased because the log has been truncated.
Keep SQL Server Management Studio open for the next demonstration.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 12: Lesson 2: Planning a Backup Strategy
Backup Types Determining Recovery Objectives Full Database Backup Strategies Transaction Log Backup Strategies Differential Backup Strategies Partial Backup Strategies Discussion: Planning Backup Strategies
Notes: Question
You have been full backups every night. A disk failure has cause major database corruption at 12 noon. The failed disk contained the primary database file but the transaction logs were stored on a separate drive. You want to ensure you can restore data that changed this morning. What kind of backup should you take before you restore the database?
( )Option 1: A full backup
( )Option 2: A differential backup
( )Option 3: A transaction log backup
( )Option 4: A tail-log backup
( )Option 5: A partial backup
Answer
(√) Option 4: A tail-log backup
20462D
4: Planning and Implementing a Backup Strategy

## Slide 13: Backup Types
Backup type | Description
Full | All data files and the active part of the transaction log
Differential | The parts of the database that have changed since the last full database backup
Transaction Log | Any database changes recorded in the log files
File/File Group | Specified files or filegroups
Partial | The primary filegroup, every read/write filegroup, and any specified read-only filegroups
Tail-log Backup | Log backup taken of the tail of the log just before a restore operation
Copy Only | The database or log (without affecting the backup sequence)
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 14: Determining Recovery Objectives
Determine safety levels:
  How long can recovering take? (RTO)
  How much data is it acceptable to lose? (RPO)
  Is it possible to recover the data from other sources?
Backup strategy should map to requirements:
  Types and frequency of backups
  Backup media to use
  Retention period for backups and for media
  Backup testing policy
Notes: Emphasize that the needs should be defined and approved with the business people who are working with the data and that the business users should know which safety level is required.
Point out that, for administrative purposes, many organizations categorize their databases based on the needs of several different available backup strategies. That way, different safety levels based on the needs of every single database can be achieved, without the requirement to test, implement and operate a special strategy for each one. A good safety level can then be achieved without too much overhead.
Discuss the RTOs and RPOs of databases in the students’ organizations.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 15: Full Database Backup Strategies
Full database backups:
Back up all data and part of the log records
Can be used to restore the whole database
Permit recovery to backup times only
Sunday
Monday
Tuesday
Notes: Discuss how to implement a full database backup strategy and its implications. Mention that a full database vbackup also serves as the base for transaction log and differential backups.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 16: Transaction Log Backup Strategies
A database and transaction log backup strategy:
Involves at least full and transaction log backups
Enables point-in-time recovery
Allows the database to be fully restored in the case of data file loss
Sunday
Monday
Notes: Describe how a database and transaction log strategy works and when it should be used. Mention that a database and transaction log is a good strategy when it is not practical to rely solely on a full database recovery strategy. Be sure to mention tail-log backups and how they are used to recover data.
Point out that log backups always contain all log records since the last transaction log backup and not just those since the full database backups.
Emphasize that a log backup strategy gives most flexibility regarding restore. They allow point-in-time recovery and it is possible to recover the database up to the last transaction, even if one or all data files are lost or corrupt. If the log file is also lost, the database can be recovered up to the point of the last backup.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 17: Differential Backup Strategies
A differential backup strategy:
Involves performing full and differential database backups
Includes differential backups with only changed data
Is useful if only a subset of a database is modified more frequently than the rest of the database
Monday
Tuesday
Notes: Differential backups always consist of all changes since the last full backup. Point out that, in the example on the slide, if the second differential backup has to be restored, only the full database backup and the second differential backup needs to be restored. The first differential backup is unnecessary because its contents are included in the second differential backup.
Make clear that a differential backup alone is useless as it cannot be restored on its own.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 18: Partial Backup Strategies
Faster backup and restore for very large databases
Can be complex to set up and manage
Monday
Tuesday
Wednesday
Thursday
Friday
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 19: Discussion: Planning Backup Strategies
For each database in the scenario, determine:
The appropriate recovery model
The type(s) of backup to be performed
The appropriate time(s) at which to perform the backup(s)
Notes: Suggested solutions are provided below. Discuss these solutions with the students.
HumanResources
Set the database to the Simple recovery model and perform a full database backup every weekday at 18:30. This ensures that the database can be recovered up to the previous day, meeting the RPO requirement. The backup should take approximately 1.4 minutes (200 MB at 150 MB/minute), and a restore can be completed in approximately two minutes (200 MB at 100 MB per minute). This more than meets the RTO requirement of an hour, even allowing for time to report the issue and locate personnel and backup media.
InternetSales
Set the database to the Full recovery model. Perform a full database backup every 12 hours (at midnight and noon), a differential backup every three hours in between full backups (at 3:00, 6:00, 9:00, 15:00, 18:00, 21:00), and a transaction log backup every 30 minutes between differential backups. The full backup will take around 1.2 hours (10 GB at 150 MB per minute), each differential backup will take around four minutes (3 x 200 MB = 600 MB at 150 MB per minute), and each log backup will take around 45 seconds (200 MB / 3 = 66.67 MB at 150 MB per minute).
In a worst case scenario, the database would fail immediately before the last transactions log backup that is scheduled before the next differential backup—for example, at 20:29. In this case, restoring the full database backup (taken at noon) will take just under 1.67 hours (10 GB / 100 MB per minute), restoring the latest available differential backup (taken at 18:00) will take around six minutes (600 MB / 100 MB per minute), and restoring the four transaction log files taken at 18:30, 19:00, 19:30, and 20:00 will take approximately 2.7 minutes (four logs, each containing 66.67 MB = 267 MB / 100 MB per minute). The total recovery time is therefore just under 1.82 hours, with a maximum data loss of 29 minutes of transactions.
AWDataWarehouse
Set the database to the Simple recovery model. Each month, back up the read-only filegroup on the last Saturday of the month after the weekly data load and monthly archiving process has completed. This will take around 11 hours for the current volume of data (100 GB / 150 MB per minute). Then on the last Sunday of the month, perform a partial backup that includes the primary filegroup and all read/write filegroups. This should take approximately 7.8 hours (50 GB + 4 x 5 GB = 70 GB / 150 MB per minute). For every other week in the month, on the Saturday after the data load batch operation has completed, perform a differential partial backup of the primary and read/write filegroups. This should take approximately 1.67 hours on the third week (3 x 5 GB = 15 GB / 150 MB per minute).
20462D
4: Planning and Implementing a Backup Strategy
(More notes on the next slide)

## Slide 20
Notes: In the event of a disaster, restore the partial database backup from the monthly backup, which should take around 11.7 hours (70 GB / 100 MB per minute), and restore the latest differential backup, which should take around 2.5 hours (15 GB / 100 MB per minute). Then restore the read-only filegroup, which should take around 16.7 hours (100 GB / 100 MB per minute). If you perform a piecemeal restore, the data in the read/write filegroup will be accessible after the differential backup has been restored (that is, after 14.2 hours). The data in the read-only filegroup will become accessible 16.7 hours later—after that filegroup has been restored. The total recovery time for the entire database is 30.9 hours.
Piecemeal restore operations are discussed in the next module.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 21: Lesson 3: Backing up Databases and Transaction Logs
Introduction to SQL Server Backup Media Sets and Backup Sets Performing Database Backups Performing Transaction Log Backups Performing Partial and Filegroup Backups Demonstration: Performing Backups
Notes: Question
You are backing up a database by using T-SQL commands. You want to back up to an existing backup set. You want to keeps the headers in the backup set but overwrite the previous backups in contains. Which of the following options should you use?
( )Option 1: INIT
( )Option 2: NOINIT
( )Option 3: FORMAT
( )Option 4: NO FORMAT
( )Option 5: DIFFERENTIAL
Answer
(√) Option 1: INIT
20462D
4: Planning and Implementing a Backup Strategy

## Slide 22: Introduction to SQL Server Backup
BACKUP { DATABASE | LOG] } <database_name>
TO <backup_device>, [,…n]
WITH <general_options>
Notes: Reassure students that specific options such as compression and encryption will be discussed in more depth later in this module.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 23: Media Sets and Backup Sets
Media sets consist of one or more disk backup devices
  Data is striped across multiple devices
A backup set represents one backup of any type
Backup sets are written to media sets
  A media set can contain multiple backup sets
Backup devices and media sets are created at first use
  Use FORMAT to overwrite an existing media set
  Use INIT to overwrite existing backup sets in a media set
  Use the FORMAT option with caution
Notes: Users are often confused by the fact that more than a single SQL Server backup can be contained within a single operating system file. The most common error related to this is to restore the first backup from a file, assuming that it is the latest version.
Use the examples in the workbook to explain how media set and backup set initialization is controlled.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 24: Performing Database Backups
Full Backup:
  Entire database
  Active portion of log file
BACKUP DATABASE AdventureWorks
TO DISK = 'R:\Backups\AW.bak'
WITH INIT;
Differential Backup
  Extents modified since the last full database backup
  Active portion of log file
BACKUP DATABASE
AdventureWorks
TO DISK = 'R:\Backups\AW.bak'
WITH DIFFERENTIAL, NOINIT;
Notes: Point out that in the example on the slide, the full database backup initializes the media set, which consists of a single file (R:\Backups\AW.bak). The differential backup is appended to the same media set, with the result that the media set contains two backup sets (the full backup and the differential backup).
Explain that it is not a requirement that differential backups be appended to the same media set as the full backup on which they are based—you could just as easily store differential backups on different media than full backups. However, should the database need to be restored from the backups, both the full backup and the latest differential backup are required; so having them on the same media set is convenient.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 25: Performing Transaction Log Backups
Backs up only the transaction log
Backs up the log from the last successfully executed log backup to the current end of the log
Truncates inactive log records unless options specified
  Note: Database must be in full or bulk-logged recovery model
BACKUP LOG AdventureWorks
TO DISK = 'R:\Backups\AW.bak'
WITH NOINIT;
BACKUP LOG AdventureWorks
TO DISK = 'R:\Backups\AW.bak'
WITH [NORECOVERY | NO_TRUNCATE | CONTINUE_ON_ERROR];
Notes: Emphasize that the database must be in FULL or BULK_LOGGED recovery mode.
Make it clear that, after switching from SIMPLE to FULL recovery model, a full database backup must be performed to create a starting point for transaction log restores.
Mention that the log is truncated after backup, unless specified via the “copy only” or “no_truncate” option.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 26: Performing Partial and Filegroup Backups
Partial Backup
  Primary filegroup
  Read/Write filegroups
File or Filegroup backup
  Specific files or filegroups
BACKUP DATABASE LargeDB
READ_WRITE_FILEGROUPS
TO DISK = 'R:\Backups\LrgRW.bak'
WITH INIT;
BACKUP DATABASE LargeDB
FILEGROUP = 'FG2'
TO DISK = 'R:\Backups\LrgFG2.bak'
Notes: Emphasize that filegroup and partial backups are typically only used when the size of a database makes it impossible to achieve the required RTO using full, differential, and transaction log backups.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 27: Demonstration: Performing Backups
In this demonstration, you will see how to:
Perform a full database backup
Perform a differential database backup
Perform a transaction log backup
Notes: Preparation Steps
Perform the previous demonstration in this module, or start the 20462C-MIA-DC and 20462C-MIA-SQL virtual machines, log on to 20462C-MIA-SQL as ADVENTUREWORKS\Student with the password Pa$$w0rd, and in the D:\Demofiles\Mod04 folder, run Setup.cmd as Administrator.
Demonstration Steps
Perform a Full Database Backup
Ensure that you have performed the previous demonstration in this module. If not, start the 20462C-MIA-DC and 20462C-MIA-SQL virtual machines, log on to 20462C-MIA-SQL as ADVENTUREWORKS\Student with the password Pa$$w0rd, and in the D:\Demofiles\Mod04 folder, run Setup.cmd as Administrator.
If SQL Server Management Studio is not already open, start it and connect to the MIA-SQL database engine using Windows authentication.
In Object Explorer, under Databases, right-click AdventureWorks, point to Tasks, and click Back Up.
In the Backup Up Database – AdventureWorks dialog box, ensure that Backup type is set to Full, and in the Destination section, select each existing file path and click Remove. Then click Add and in the Select Backup Destination dialog box, enter the file name D:\Demofiles\Mod04\AW.bak and click OK.
In the Backup Up Database – AdventureWorks dialog box, on the Media Options page, note that the default option is to append to an existing media set. In this case, there is no existing media set so a new one will be created, and there are no existing backup sets to overwrite.
In the Backup Up Database – AdventureWorks dialog box, on the Backup Options page, note the default backup name and expiration settings.
In the Backup Up Database – AdventureWorks dialog box, in the Script drop-down list, click Script Action to a New Query Window. Then click OK.
When the backup has completed successfully, click OK.
In the query pane, view the Transact-SQL BACKUP statement that was used to back up the database.
View the D:\Demofiles\Mod04 folder and note the size of the AW.bak file.
20462D
4: Planning and Implementing a Backup Strategy
(More notes on the next slide)

## Slide 28
Notes: Perform a Differential Backup
In SQL Server Management Studio, open the UpdatePrices.sql script file from the D:\Demofiles\Mod04 folder and click Execute. This script updates the Production.Product table in the AdventureWorks database.
In Object Explorer, under Databases, right-click AdventureWorks, point to Tasks, and click Back Up.
In the Backup Up Database – AdventureWorks dialog box, in the Backup type list, select Differential. Then in the Destination section, ensure that D:\Demofiles\Mod04\AW.bak is the only backup device listed.
In the Backup Up Database – AdventureWorks dialog box, on the Media Options page, verify that the option to append to the existing media set is selected.
In the Backup Up Database – AdventureWorks dialog box, on the Backup Options page, change the Name to AdventureWorks-Diff DatabaseBackup.
In the Backup Up Database – AdventureWorks dialog box, in the Script drop-down list, click Script Action to a New Query Window. Then click OK.
When the backup has completed successfully, click OK.
In the query pane, view the Transact-SQL BACKUP statement that was used to back up the database. Note that it includes the WITH DIFFERENTIAL option.
View the D:\Demofiles\Mod04 folder and note that size of the AW.bak file has increased, but not much – the second backup only includes the extents containing pages that were modified since the full backup.
(More notes on the next slide)
20462D
4: Planning and Implementing a Backup Strategy

## Slide 29
Notes: Perform a Transaction Log Backup
In SQL Server Management Studio, switch to the UpdatePrices.sql script you opened previously and click Execute to update the Production.Product table in the AdventureWorks database again.
In Object Explorer, under Databases, right-click AdventureWorks, point to Tasks, and click Back Up.
In the Backup Up Database – AdventureWorks dialog box, in the Backup type list, select Transaction Log. Then in the Destination section, ensure that D:\Demofiles\Mod04\AW.bak is the only backup device listed.
In the Backup Up Database – AdventureWorks dialog box, on the Media Options page, verify that the option to append to the existing media set is selected. Also verify that the option to truncate the transaction log is selected.
In the Backup Up Database – AdventureWorks dialog box, on the Backup Options page, change the Name to AdventureWorks-Transaction Log Backup.
In the Backup Up Database – AdventureWorks dialog box, in the Script drop-down list, click Script Action to a New Query Window. Then click OK.
When the backup has completed successfully, click OK.
In the query pane, view the Transact-SQL BACKUP statement that was used to back up the database. Note that this time the statement is BACKUP LOG.
View the D:\Demofiles\Mod04 folder and note that size of the AW.bak file has increased, but not much – the third backup only includes the transaction log entries for data modifications since the full backup.
Keep SQL Server Management Studio open for the next demonstration.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 30: Lesson 4: Using Backup Options
Copy-Only Backups Compressing Backups Demonstration: Using Backup Compression Encrypting Backups Demonstration: Using Backup Encryption
Notes: Question
You want to use encrypted backups to protect your system against disasters and ensure backups are secured against unauthorized access. What encryption keys must you create?
Answer
A database master key and an asymmetric encryption key or a certificate.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 31: Copy-Only Backups
Back up the database without changing the restore order
Copy-only transaction log backups do not truncate the log
Copy-only full database backups do not affect the differential base
BACKUP DATABASE AdventureWorks
TO DISK = 'Q:\Backups\AW_Copy.bak'
WITH COPY_ONLY, INIT;
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 32: Compressing Backups
Reduces size of backup on device
Reduces I/O requirements, increases CPU usage
Increases speed of backup and restore
Some restrictions:
  Cannot share media with uncompressed backups
  Cannot share media with Windows backups
  Cannot be restored to pre-2008 SQL Server versions
BACKUP DATABASE AdventureWorks
TO DISK = 'R:\Backups\AW_Comp.bak'
WITH COMPRESSION;
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 33: Demonstration: Using Backup Compression
In this demonstration, you will see how to:
Use backup compression.
Notes: Preparation Steps
Perform the previous demonstration in this module.
Demonstration Steps
Use Backup Compression
Ensure that you have performed the previous demonstration in this module.
In SQL Server Management Studio, in Object Explorer, under Databases, right-click AdventureWorks, point to Tasks, and click Back Up.
In the Backup Up Database – AdventureWorks dialog box, ensure that Backup type is set to Full, and in the Destination section, select the existing file path and click Remove. Then click Add and in the Select Backup Destination dialog box, enter the file name D:\Demofiles\Mod04\AW_Comp.bak and click OK.
In the Backup Up Database – AdventureWorks dialog box, on the Media Options page, note that the default option is to append to an existing media set. In this case, there is no existing media set so a new one will be created, and there are no existing backup sets to overwrite.
In the Backup Up Database – AdventureWorks dialog box, on the Backup Options page, change the Name to AdventureWorks-Compressed Backup and in the Set backup compression list, select Compress backup.
In the Backup Up Database – AdventureWorks dialog box, in the Script drop-down list, click Script Action to a New Query Window. Then click OK.
When the backup has completed successfully, click OK.
In the query pane, view the Transact-SQL BACKUP statement that was used to back up the database, noting that the COMPRESSION option was specified.
View the D:\Demofiles\Mod04 folder and note the size of the AW_Comp.bak file. This should be significantly smaller than the AW.bak file was after the full database backup in the previous demonstration.
Keep SQL Server Management Studio open for the next demonstration.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 34: Encrypting Backups
Create a database master key for master
Create a certificate or asymmetric key
Back up the database, specifying the algorithm and key
BACKUP DATABASE AdventureWorks
TO DISK = 'R:\Backups\AW_Encrypt,bak'
WITH FORMAT, INIT,
ENCRYPTION( ALGORITHM = AES_128,
SERVER CERTIFICATE = [BackupCert])
Notes: Encrypted backups were introduced in SQL Server 2014. In prior releases, you could protect backup media by encrypting the entire database (using Transparent Database Encryption) before backing it up. However, this approach resulted in large backup files and impacted backup performance.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 35: Demonstration: Using Backup Encryption
In this demonstration, you will see how to:
Create a database master key.
Create a certificate.
Encrypt a database backup.
Notes: Preparation Steps
Complete the previous demonstration in this module.
Demonstration Steps
Create a Database Master Key
Ensure that you have performed the previous demonstration in this module.
In SQL Server Management Studio, open the EncyptionKeys.sql script file in the D:\Demofiles\Mod04 folder.
Select the code under the comment Create a database master key and click Execute.
Select the code under the comment Back up the database master key and click Execute.
Create a Certificate
Select the code under the comment Create a certificate and click Execute.
Select the code under the comment Back up the certificate and its private key and click Execute.
Encrypt a Database Backup
In Object Explorer, under Databases, right-click AdventureWorks, point to Tasks, and click Back Up.
In the Backup Up Database – AdventureWorks dialog box, ensure that Backup type is set to Full, and in the Destination section, select the existing file path and click Remove. Then click Add and in the Select Backup Destination dialog box, enter the file name D:\Demofiles\Mod04\AW_Encrypt.bak and click OK.
In the Backup Up Database – AdventureWorks dialog box, on the Media Options page, select Back up to a new media set, and erase all existing backup sets. Then enter the new media set name Encrypted Backup.
In the Backup Up Database – AdventureWorks dialog box, on the Backup Options page, change the Name to AdventureWorks-Encrypted Backup and in the Set backup compression list, select Compress backup.
20462D
4: Planning and Implementing a Backup Strategy
(More notes on the next slide)

## Slide 36
Notes: In the Encryption section, select Encrypt backup. Then ensure that the AES 128 algorithm is selected, and select the BackupCert certificate you created previously.
In the Backup Up Database – AdventureWorks dialog box, in the Script drop-down list, click Script Action to a New Query Window. Then click OK.
When the backup has completed successfully, click OK.
In the query pane, view the Transact-SQL BACKUP statement that was used to back up the database, noting that the ENCRYPTION option was specified.
Keep SQL Server Management Studio open for the next demonstration.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 37: Lesson 5: Ensuring Backup Reliability
Determining a Retention and Testing Policy for Backups Options for Ensuring Backup Integrity Viewing Backup History Retrieving Backup Metadata Demonstration: Verifying Backups
Notes: Question
You have been experimenting with database backups and restores in order to create a reliable disaster recovery strategy. Now you want to remove the records of backups from the HumanResources database because you have deleted the test backups you created. What T-SQL command should you execute?
Answer
EXEC sp_delete_database_backuphistory @database_name = 'HumanResources';
20462D
4: Planning and Implementing a Backup Strategy

## Slide 38: Determining a Retention and Testing Policy for Backups
Planning for backup retention must be part of the strategy and form part of the test plan to ensure accuracy
Several considerations:
  Combination of backups needed for a database recovery
  Archival requirements
  Synchronization with database checks
  Available secure storage location
  Hardware required for restoring backups
  Completeness of backups
Notes: Note: Most of the slide topics relate to the "General Considerations" section in the student notes.
Discuss the considerations required to plan a retention policy, and the backups that are needed for a database recovery when several backup types are combined together.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 39: Options for Ensuring Backup Integrity
Mirrored media sets:
Can mirror a backup set to up to four media sets
Mirrors require the same number of backup devices
Only in Enterprise Edition
CHECKSUM backup option
Available for all backup types
Generates a checksum over the backup stream
Use to verify the backup
Backup verification
Can use RESTORE VERIFYONLY for backup verification
Useful when combined with the CHECKSUM option
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 40: Viewing Backup History
SQL Server tracks all backup activity in a set of tables in the msdb database
The Backup and Restore Events report in SQL Server Management Studio displays detailed backup history information
  SELECT bs.media_set_id, bs.backup_finish_date, bs.type,
  bs.backup_size, bs.compressed_backup_size,
  mf.physical_device_name
  FROM dbo.backupset AS bs
  INNER JOIN dbo.backupmediafamily AS mf
  ON bs.media_set_id = mf.media_set_id
  WHERE database_name = 'AdventureWorks'
  ORDER BY backup_finish_date DESC;
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 41: Retrieving Backup Metadata
RESTORE LABELONLY returns information about the backup media on a specified backup device
RESTORE HEADERONLY returns all the backup header information for all backup sets on a particular backup device
RESTORE FILELISTONLY returns a list of data and log files contained in a backup set
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 42: Demonstration: Verifying Backups
In this demonstration, you will see how to:
View the backup and Restore Events report.
Query backup history tables.
Verify backup media.
Notes: Preparation Steps
Complete the previous demonstrations in this module.
Demonstration Steps
View the Backup and Restore Events Report
Ensure that you have performed the previous demonstration in this module.
In SQL Server Management Studio, in Object Explorer, under Databases, right-click AdventureWorks, point to Reports, point to Standard Reports, and click Backup and Restore Events.
In the Backup and Restore Events [AdventureWorks] report, expand Successful Backup Operations and view the backup operations that have been performed for this database.
In the Device Type column, expand each of the Disk (temporary) entries to view details of the backup media set files.
Query Backup History Tables
In SQL Server Management Studio, open the VerifyingBackups.sql script file in the D:\Demofiles\Mod04 folder.
Select the code under the comment View backup history, and click Execute.
View the query results.
Verify Backup Media
Select the code under the comment Use RESTORE HEADERONLY, and click Execute.
View the query results, which show the backups in the AW.bak backup device.
Select the code under the comment Use RESTORE FILELISTONLY, and click Execute.
View the query results, which show the database files contained in the backups.
Select the code under the comment Use RESTORE VERIFYONLY, and click Execute.
View the message that is returned, which should indicate that the backup is valid.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 43: Lab: Backing Up Databases
Exercise 1: Backing Up Databases Exercise 2: Performing Database, Differential, and Transaction Log Backups Exercise 3: Performing a Partial Backup
Logon Information
Virtual machine: 20462C-MIA-SQL
User name: ADVENTUREWORKS\Student
Password: Pa$$w0rd
Estimated Time: 90 minutes
Notes: Exercise 1: Backing Up Databases
The backup strategy for the HumanResources database is based on daily full database backups. You must perform tests of these backup operations and verify the backups.
Exercise 2: Performing Database, Differential, and Transaction Log Backups
The backup strategy for the InternetSales database uses a combination of full, differential, and transaction log backups.
Exercise 3: Performing a Partial Backup
The AWDataWarehouse database is too large for a conventional backup strategy, so you have decided to use a partial backup strategy.
20462D
4: Planning and Implementing a Backup Strategy

## Slide 44: Lab Scenario
As a database administrator for Adventure Works Cycles, you are responsible for the HumanResources, InternetSales, and AWDataWarehouse databases. You must implement a backup solution for these databases, based on the backup requirements that have been provided.
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 45: Lab Review
In this lab, you have seen how to set the recovery model for a database based on its backup strategy, and how to perform full, differential, transaction log, filegroup, and partial backups.
Notes: 20462D
4: Planning and Implementing a Backup Strategy

## Slide 46: Module Review and Takeaways
Review Question(s) Best Practice
Notes: Review Question(s)
Question
What are the unique features of transaction log restores?
Answer
Point-in-time recovery and the ability to restore up to the point of failure if only data files are corrupt.
Question
When might a full database backup strategy be adequate?
Answer
If it is sufficient, in case of a disaster, to restore the database to the points of full database backup only.
Best Practice:
Plan your backup strategy carefully.
Plan the backup strategy in conjunction with the business needs.
Choose the appropriate database recovery model.
Plan your transaction log size based on the transaction log backup frequency.
Consider using differential backups to speed recovery.
Consider compressing backups to reduce storage requirements and backup time.
20462D
4: Planning and Implementing a Backup Strategy