## Slide 1: Module 7
Monitoring SQL Server 2014
Notes: The 20462C-MIA-SQL virtual machine used in the lab for this module includes a lot of software services that can take a while to start. For the best experience, have students start the 20462C-MIA-DC and 20462C-MIA-SQL virtual machines at the beginning of the module so that the services have time to start before students begin the lab.
20462D
7: Monitoring SQL Server 2014

## Slide 2: Module Overview
Introduction to Monitoring SQL Server Dynamic Management Views and Functions Performance Monitor
Notes: 20462D
7: Monitoring SQL Server 2014

## Slide 3: Lesson 1: Introduction to Monitoring SQL Server
SQL Server Monitoring Overview Monitoring Tools for SQL Server Activity Monitor Demonstration: Using Activity Monitor
Notes: Question
You want to record the performance of both Windows and SQL Server on a specific machine so that you can analyze it later by examining data on a single graph. Which of the following tools should you use?
( )Option 1: Activity Monitor in SSMS
( )Option 2: Dynamic Management Views
( )Option 3: Dynamic Management Functions
( )Option 4: Performance Monitor
( )Option 5: Distributed Replay
Answer
(√) Option 4: Performance Monitor
20462D
7: Monitoring SQL Server 2014

## Slide 4: SQL Server Monitoring Overview
Why monitor?
  Diagnose causes of performance issues
  Detect and resolve concurrency problems
  Identify changing trends in resource utilization
Guidelines for monitoring
  Understand the workloads you need to support
  Establish a baseline
  Monitor regularly to track changes in key metrics
Notes: Point out that resolving concurrency problems usually requires further exploration of the workloads. Techniques for tracing workloads and resolving lock-related issues are discussed in the next module
20462D
7: Monitoring SQL Server 2014

## Slide 5: Monitoring Tools for SQL Server
Activity Monitor
Dynamic Management Views and Functions
Performance Monitor
SQL Server Profiler
SQL Trace
Database Engine Tuning Advisor
Distributed Replay
SQL Server Data Collection
SQL Server Utility Control Point
Microsoft System Center Operations Manager
Notes: Point out that this module focuses on Activity Monitor, DMVs and DMFs, and Performance Monitor. SQL Server Profiler, SQL Trace, and the Database Engine Tuning Advisor are covered in the next module of this course. To learn how to configure SQL Server Data Collection and SQL Server Utility Control Point, students should attend course 20465C: Designing a Data Solution with Microsoft SQL Server.
20462D
7: Monitoring SQL Server 2014

## Slide 6: Activity Monitor
Shows information about:
  SQL Server processes
  Waits
  I/O
  Resource performance
  Expensive queries
Requires VIEW SERVER STATE permissions
Notes: Explain that you can use Activity Monitor to investigate both current issues such as "Is one process being blocked by another process?" and recent historical issues such as "Which query has taken the most resources since the server was last restarted?"
20462D
7: Monitoring SQL Server 2014

## Slide 7: Demonstration: Using Activity Monitor
In this demonstration, you will see how to:
View server activity in Activity Monitor
Troubleshoot a blocked process
Notes: Troubleshooting locking issues is discussed in more depth in the next module.
Preparation Steps
Start the 20462C-MIA-DC, and 20462C-MIA-SQL virtual machines.
Demonstration Steps
View Server Activity in Activity Monitor
Ensure that the 20462C-MIA-DC, and 20462C-MIA-SQL virtual machines are running, and log on to 20462C-MIA-SQL as ADVENTUREWORKS\Student with the password Pa$$w0rd.
In the D:\Demofiles\Mod07 folder, run Setup.cmd as Administrator.
Start SQL Server management Studio and connect to the MIA-SQL database engine instance using Windows authentication.
In Object Explorer, right-click the MIA-SQL SQL Server instance and click Activity Monitor.
In Activity Monitor, view the charts in the Overview section, which show background activity in the SQL Server instance.
Expand the Processes section and view the processes currently running in the SQL Server instance.
Click the filter icon for the Application column header, and filter the data to show only processes for the Microsoft SQL Server Management Studio application (you may need to widen the columns to read the headers).
Remove the filter to show all applications.
Expand the Resource Waits section and view the statistics for processes waiting on resources.
Expand the Data File I/O section and view the details of the database file I/O activity (you may need to wait for a few seconds while the data is collected and displayed).
Expand the Recent Expensive Queries section and view the list of queries that have consumed query processing resources.
20462D
7: Monitoring SQL Server 2014
(More notes on the next slide)

## Slide 8
Notes: Troubleshoot a Blocked Process
With Activity Monitor still open in SQL Server Management Studio, in the D:\Demofiles\Mod07 folder, run ActivityWorkload.cmd.
In SQL Server Management Studio, in Object Explorer, expand Databases, expand AdventureWorks, and expand Tables. Then right-click Production.Product and click Select Top 1000 Rows.
In status bar at the bottom of the query pane, note that the query continues executing. Another process is preventing it from completing.
In the Activity Monitor pane, in the Processes section, filter the Task State column to show processes that are in a SUSPENDED state.
In the Blocked By column for the suspended process, note the ID of the process that is blocking this one.
Remove the filter on the Task State column to show all processes, and find the blocking process with the ID you identified in the previous step.
Note the value in the Head Blocker column for the blocking process. A value of 1 indicates that this process is the first one in a chain that is blocking others.
Right-click the blocking process and click Details. This displays the Transact-SQL code that is causing the block—in this case, a transaction that has been started but not committed or rolled back.
Click Kill Process, and when prompted to confirm, click Yes. After a few seconds, the Processes list should update to show no blocked processes.
Close the Activity Monitor pane, and verify that the query to retrieve the top 1000 rows from Production.Products has now completed successfully.
Close the command prompt window, but keep SQL Server Management Studio open for the next demonstration.
20462D
7: Monitoring SQL Server 2014

## Slide 9: Lesson 2: Dynamic Management Views and Functions
Overview of Dynamic Management Views and Functions Viewing Activity by Using Dynamic Management Views Demonstration: Querying Dynamic Management Views
Notes: Question
A new DBA in your team has been trying to use the sys.dm_db_index_usage_stats view in a query to monitor performance but has been denied access. Which permission should you grant him?
Answer
Grant the VIEW DATABASE STATE permission.
20462D
7: Monitoring SQL Server 2014

## Slide 10: Overview of Dynamic Management Views and Functions
Virtual views and functions that provide dynamic system data at server and database level
Category | Description
sys.dm_exec_% | Execution and connection information
sys.dm_os_% | Operating system related information
sys.dm_tran_% | Transaction management information
sys.dm_io_% | I/O related information
sys.dm_db_% | Database information
Notes: 20462D
7: Monitoring SQL Server 2014

## Slide 11: Viewing Activity by Using Dynamic Management Views
SELECT s.original_login_name, s.program_name, t.wait_type, t.wait_duration_ms
FROM sys.dm_os_waiting_tasks AS t
INNER JOIN sys.dm_exec_sessions AS s
ON t.session_id = s.session_id
WHERE s.is_user_process = 1
AND t.wait_duration_ms > 3000;
SELECT * FROM sys.dm_os_wait_stats
ORDER BY wait_time_ms DESC;
Must reference using the sys schema
Two basic types:
  Real-time state information
  Historical information
Notes: Note: In the table in the student notes, we are using the Transact-SQL wildcard character % which means any number of characters in this position. We are aware that the underscore character is also a wildcard, but we felt that specifying dm[_]% as the DMV naming convention would be distracting or misleading.
20462D
7: Monitoring SQL Server 2014

## Slide 12: Demonstration: Querying Dynamic Management Views
In this demonstration, you will see how to:
View SQL Server service configuration settings
View storage volume statistics
View query statistics
Notes: Explain that DBCC FREEPROCCACHE clears the plan cache, and point out that it should be used with caution on production servers as clearing the plan cache can have a detrimental effect on query performance.
Preparation Steps
Complete the previous demonstration in this module. Alternatively, start the 20462C-MIA-DC, and 20462C-MIA-SQL virtual machines, log on to 20462C-MIA-SQL as ADVENTUREWORKS\Student with the password Pa$$w0rd, and in the D:\Demofiles\Mod07 folder, run Setup.cmd as Administrator.
Demonstration Steps
View SQL Server Service Configuration Settings
If you did not complete the previous demonstration in this module, start the 20462C-MIA-DC, and 20462C-MIA-SQL virtual machines, log on to 20462C-MIA-SQL as ADVENTUREWORKS\Student with the password Pa$$w0rd, and in the D:\Demofiles\Mod07 folder, run Setup.cmd as Administrator.
If SQL Server Management Studio is not already open, start it and connect to the MIA-SQL database engine instance using Windows authentication.
In SQL Server Management Studio, open the DMVs.sql script file in the D:\Demofiles\Mod07 folder.
Highlight the Transact-SQL statement under the comment View service information, and then click Execute.
Review the results, noting the values in the startup_type column for the SQL Server and SQL Server Agent services.
Highlight the Transact-SQL statement under the comment View registry information, and then click Execute.
Review the results. Note the value Start in the value_name column for the MSSQLSERVER and SQLSERVERAGENT registry keys and the corresponding values in the value_data column. These values are the equivalent registry value for the startup_type column values returned by the sys.dm_server_services dynamic management view.
20462D
7: Monitoring SQL Server 2014
(More notes on the next slide)

## Slide 13
Notes: View SQL Server Service Configuration Settings
If you did not complete the previous demonstration in this module, start the 20462C-MIA-DC, and 20462C-MIA-SQL virtual machines, log on to 20462C-MIA-SQL as ADVENTUREWORKS\Student with the password Pa$$w0rd, and in the D:\Demofiles\Mod07 folder, run Setup.cmd as Administrator.
If SQL Server Management Studio is not already open, start it and connect to the MIA-SQL database engine instance using Windows authentication.
In SQL Server Management Studio, open the DMVs.sql script file in the D:\Demofiles\Mod07 folder.
Highlight the Transact-SQL statement under the comment View service information, and then click Execute.
Review the results, noting the values in the startup_type column for the SQL Server and SQL Server Agent services.
Highlight the Transact-SQL statement under the comment View registry information, and then click Execute.
Review the results. Note the value Start in the value_name column for the MSSQLSERVER and SQLSERVERAGENT registry keys and the corresponding values in the value_data column. These values are the equivalent registry value for the startup_type column values returned by the sys.dm_server_services dynamic management view.
View Storage Volume Statistics
Select the Transact-SQL code under the comment View volume stats, noting that it retrieves data from the sys.sysdatabases and sys.master_files system tables as well as the sys.dm_os_volume_stats dynamic management function.
Click Execute and review the query results, which show the files for all databases in the instance, together with details about the disk volume on which they are hosted.
(More notes on the next slide)
20462D
7: Monitoring SQL Server 2014

## Slide 14
Notes: View Query Statistics
Highlight the Transact-SQL statement under the comment Empty the cache and then click Execute.
Highlight the Transact-SQL statement under the comment get query stats, noting that this code uses the sys.dm_exec_query_stats DMV and the sys.dm_exec_sql_text DMF to return details about Transact-SQL queries that have been executed.
Click Execute and review the results, which show some background system queries, noting the various columns that are returned.
Highlight the Transact-SQL statement under the comment Execute a query, and then click Execute.
Re-highlight the Transact-SQL statement under the comment get query stats, and then click Execute to get the query stats again.
In the results, find the row with a SQLText column that contains the Transact-SQL statement that you executed and note the statistics returned for the query.
Re-highlight the Transact-SQL statement under the comment Execute a query, and then click Execute to run the query again.
Re-highlight the Transact-SQL statement under the comment get query stats, and then click Execute to get the query stats again.
Review the results for the query, noting that the query you executed now has an execution_count value of 2.
Close SQL Server Management Studio without saving any files.
20462D
7: Monitoring SQL Server 2014

## Slide 15: Lesson 3: Performance Monitor
Introduction to Performance Monitor SQL Server Counters Data Collector Sets and Logs Demonstration: Using Performance Monitor
Notes: 20462D
7: Monitoring SQL Server 2014

## Slide 16: Introduction to Performance Monitor
Collects and displays system metrics
  Objects: system resource categories
  Counters: Metrics that can be measured
  Instances: Individual instances of multi-instance objects
Charts and Reports
  Line chart
  Histogram bar chart
  Text-based report
Object: Processor
Counter:
% Processor Time
Instances:
_Total
CPU0
CPU1
CPU2
CPU3
Notes: Emphasize that Performance Monitor is the key tool for monitoring Windows systems. Its value comes from being able to monitor the system as a whole, rather than just from the perspective of a single SQL Server instance.
Note that, at the Windows level, the main focus lies on CPU, memory, disk system and network. Ensure that students are clear that instances of counters is not related to instances of SQL Server, unless referring to the SQL Server object.
20462D
7: Monitoring SQL Server 2014

## Slide 17: SQL Server Counters
SQL Server exposes objects to Performance Monitor
  SQLServer:<object> (default SQL Server instance)
  MSSQL$<instance>:<object> (named SQL Server instance)
  SQLAgent$<instance>:<object> (SQL Server Agent)
Query performance counters using the sys.dm_os_performance_counters DMV
Notes: 20462D
7: Monitoring SQL Server 2014

## Slide 18: Data Collector Sets and Logs
Group counters into reusable Data Collector Sets
Run Data Collector Sets to log counter values
View logs in Performance Monitor
Notes: 20462D
7: Monitoring SQL Server 2014

## Slide 19: Demonstration: Using Performance Monitor
In this demonstration, you will see how to:
View performance counters
Notes: The % Processor Time counter measures how much of the time the computer’s CPU is actively in use. A consistently high value for this counter might mean that the workloads on the server require more CPU resources than are available (they are “CPU-bound”), and a faster CPU (or more CPUs) might be required.
The Page Faults/sec counter measures how often Windows needs to retrieve a memory pages from the “swap file” on disk. A consistently high value for this counter may indicate a shortage of physical memory, and workloads may be “memory-bound”.
The SQLServer:Locks object provides counters that enable you to observe locking activity in SQL Server. A high value for Lock requests/sec in itself simply means that there are a lot of transactions that need exclusive access to data rows, pages, or tables. A consistently high value for Average wait time (ms) or Lock waits/sec might indicate that database workloads are experiencing concurrency issues as multiple applications try to access the same data.
The SQLServer:Plan Cache object enables you to monitor utilization of cached query plans. A high Cache hit ratio value means that the database workloads frequently re-use the same Transact-SQL queries, and the execution plans for these queries has been compiled and cached to improve performance.
The SQLServer:Transactions object provides statistics for transactions in SQL Server. A high transactions value indicates a lot of transactional activity that accesses and modifies data.
Preparation Steps
Complete the previous demonstration in this module. Alternatively, start the 20462C-MIA-DC, and 20462C-MIA-SQL virtual machines, log on to 20462C-MIA-SQL as ADVENTUREWORKS\Student with the password Pa$$w0rd, and in the D:\Demofiles\Mod07 folder, run Setup.cmd as Administrator.
Demonstration Steps
View Performance Counters
If you did not complete the previous demonstration in this module, start the 20462C-MIA-DC, and 20462C-MIA-SQL virtual machines, log on to 20462C-MIA-SQL as ADVENTUREWORKS\Student with the password Pa$$w0rd, and in the D:\Demofiles\Mod07 folder, run Setup.cmd as Administrator.
Right-click the Start button and click Computer Management.
In Computer Management, expand Performance, expand Monitoring Tools, and click Performance Monitor.
In the toolbar, click the Add button (a green +).
20462D
7: Monitoring SQL Server 2014
(More notes on the next slide)

## Slide 20
Notes: In the list of objects, expand the Processor object, and select only the % Processor Time counter. Then in the Instances of selected object list, ensure that _Total is selected and click Add.
In the list of objects, expand the Memory object and select the Page Faults/sec counter. Then click Add.
In the list of objects, expand the SQLServer:Locks object, click the Average Wait Time (ms) counter, and then hold the Ctrl key and click the Lock Requests/sec and Lock Waits/sec counters. Then in the Instances of selected object list, ensure that _Total is selected and click Add.
In the list of objects, expand the SQLServer:Plan Cache object, and select the Cache Hit Ratio counter. Then in the Instances of selected object list, ensure that _Total is selected and click Add.
In the list of objects, expand the SQLServer:Transactions object, and select the Transactions counter. Then click Add.
In the Add Counters dialog box, click OK. Then observe the counters as they are displayed in Performance Monitor.
On the toolbar, click Freeze Display and note that the chart is paused. Then click Unfreeze Display to resume the chart.
On the toolbar, in the Change Graph Type list, select Histogram bar and view the resulting chart. Then in the Change Graph Type list, select Report and view the text-based report.
On the toolbar, in the Change Graph Type list, select Line to return to the original line chart view.
Click any of the counters in the list below the chart and on the toolbar click Highlight so that the selected counter is highlighted in the chart. Press the up and down arrow keys on the keyboard to change the selected counter.
In the D:\Demofiles\Mod07 folder, run PerformanceWorkload1.cmd and PerformanceWorkload2.cmd to generate some activity in the database.
In Performance Monitor, observe the effect on the counters as the workloads run.
Close both command prompt windows, and observe the effect that ending the workloads has on the Performance Monitor counters.
Close Computer Management.
20462D
7: Monitoring SQL Server 2014

## Slide 21: Lab: Monitoring SQL Server 2014
Exercise 1: Collecting Baseline Metrics Exercise 2: Monitoring a Workload
Logon Information
Virtual machine: 20462C-MIA-SQL
User name: ADVENTUREWORKS\Student
Password: Pa$$w0rd
Estimated Time: 45 minutes
Notes: Exercise 1: Collecting Baseline Metrics
The InternetSales database is the data source for a business-critical application. You need to record measurements of key performance metrics for this database to establish a performance baseline.
Exercise 2: Monitoring a Workload
The application developers of the Adventure Works e-commerce solution have added some new reporting capabilities to the application. You need to determine how these new capabilities have affected the workload for the InternetSales database.
20462D
7: Monitoring SQL Server 2014

## Slide 22: Lab Scenario
You are a database administrator (DBA) at Adventure Works Cycles with responsibility for the InternetSales database. One of your key tasks is to monitor this database to ensure that it is performing within expected parameters.
Notes: 20462D
7: Monitoring SQL Server 2014

## Slide 23: Lab Review
Based on the results of your monitoring, what aspect of the database solution is most significantly affected by the changes to the workload?
Notes: Question
Based on the results of your monitoring, what aspect of the database solution is most significantly affected by the changes to the workload?
Answer
The number of lock requests, wait time, and I/O statistics should be relatively unchanged between the baseline and the revised workload. The biggest change is the increased requirement for memory, shown by an increase in the number of page faults, a higher average database cache memory figure, and a reduced free memory figure.
The main cause for the increased memory requirements is a query that declares a table variable and inserts details of every order into it.
20462D
7: Monitoring SQL Server 2014

## Slide 24: Module Review and Takeaways
Review Question(s) Best Practice
Notes: Review Question(s)
Question
How are dynamic management views and functions different from system tables?
Answer
Dynamic management views and functions that are virtual objects, providing access to state information. The data they provide is accessed dynamically and is not persisted between server restarts.
Best Practice: When monitoring SQL Server, consider the following best practices:
Identify the system resources that your database workload uses, and determine the key performance metrics that indicate how your database and server are performing.
Record baseline measurements for typical and peak workloads so that you have a basis for comparison when troubleshooting performance problems later.
Identify the DMVs and DMFs that return appropriate performance information for your workloads, and create reusable scripts that you can use to quickly check system performance.
Monitor the overall system periodically and compare the results with the baseline. This can help you detect trends that will eventually result in resource over-utilization before application performance is affected.
20462D
7: Monitoring SQL Server 2014